## Slide 1
GEOSldas Tutorial and Land Model Versions
Weiyuan Jiang, Sarith Mahanama, Justin Perket, and Rolf Reichle
Original version: 11 September 2017
Last updated: 04 September 2019
LDAS tag: GEOSldas_m4-17_7
Location in src code: ./src/Applications/LDAS_App/doc/

## Slide 2
Table of Contents
Summary of GEOSldas
GEOSldas Tutorial
  Check out, build and prepare for ldas_setup
  Configure experiment
  Configure computing resources
  Run ldas_setup to create an experiment for model or assimilation runs
  Resource files created by ldas_setup
  Run GEOSldas
  Using graphic debugger tools
  Documentation and utilities for post-processing
Land Model Versions
Additional Parameters for the AGCM

## Slide 3
1. Summary of GEOSldas
“GEOSldas” is the software of the stand-alone land modeling and assimilation components of the Goddard Earth Observing System (GEOS) model. GEOSldas is a fully ESMF-compliant successor of the legacy “LDASsa” software suite and supports discretizations (tiles) on the lat/lon, EASE, and cube-sphere grids.
The CVS tag GEOSldas_m4-17_7 includes model components for Catchment and CatchmentCN. It also includes assimilation components for Catchment. The science version is the equivalent of the reichle-LDASsa_m3-16_6_p1 LDASsa tag (used to generate the Version 4 SMAP L4_SM product). New configuration parameters (LAND_PARAMS) replace the LAND_UPD compiler flag (see below).
History of recent stable tags: GEOSldas_m4-17_7
GEOSldas_m4-17_6
GEOSldas_m4-17_0

## Slide 4
1. Summary of GEOSldas
GEOSldas_m4-17_6 is a model-only tag that matches the science version of the LDASsa tag reichle-LDASsa_m3-16_6. The execution time for the cube-sphere grid is improved through better load balancing. The tag includes some assimilation components but these are not working, and it also does not work with CatchmentCN.
The tag GEOSldas_m4-17_0 is the first ever stable GEOSldas tag. It includes only the land model (and ensemble perturbations). The assimilation components do not work! The tag combines a new CVS module (“m4”) with a new science version of the Catchment model (“17_0”; see section “Land Model Versions” of this tutorial). Both Catchment and CatchmentCN are supported, as is the snow impurity module (GOSWIM).

## Slide 5
  2.a) Check out, build and prepare for ldas_setup
See https://github.com/GEOS-ESM/GEOSldas for README.md details
Check Out :
  module use -a /discover/swdev/gmao_SIteam/modulefiles-SLES11 #NCCS
  module load GEOSenv
  git clone git@github.com:GEOS-ESM/GEOSldas.git
Check out external repositories and build in one step:
  parallel_build.csh
  Can use do multiple steps: see README.md
  Verify build:
  cat build/BUILD_LOG_DIR/info

## Slide 6
  2.a) Check out, build and prepare for ldas_setup
Prepare for ldas_setup (go to install/bin , source g5_modules if it is a new terminal window ):
./ldas_setup –h (show help for ldas_setup)
./ldas_setup sample –h (show help for sub-command “sample”)
./ldas_setup setup –h (show help for sub-command “setup”)
Create input templates:
./ldas_setup sample –-exeinp > YOUR_exeinp.txt
./ldas_setup sample –-batinp > YOUR_batinp.txt

## Slide 7
  Edit the sample input file YOUR_exeinp.txt created by the following command:
  ./ldas_setup sample –-exeinp> YOUR_exeinp.txt
###########################################################################
# EXPERIMENT INFO #
###########################################################################
EXP_ID : merra2_cf180
EXP_DOMAIN : CF0180x6C_CONUS
NUM_ENSEMBLE : 1
BEG_DATE : 20140101 000000
END_DATE : 20140301 000000
###########################################################################
# RESTART INFO #
###########################################################################
RESTART : 0
#RESTART_ID : SMAP_Nature_v4.1
#RESTART_PATH : /discover/nobackup/users/MERRA3/SMAP_Nature_v4.1/
#RESTART_DOMAIN : SMAP_EASEv2_M36_GLOBAL
**** REQUIRED INFO *****
RESTART : 1
Have restarts from
a GEOSldas simulation on the same grid and the same or larger domain or
a global LDASsa simulation on the same grid.
  2.b) Configure experiment

## Slide 8
###########################################################################
# METEOROLOGICAL FORCINGS #
###########################################################################
MET_TAG : M2COR_cross
MET_PATH : /discover/nobackup/projects/gmao/merra/iau/merra_land/MERRA2_land_forcing/
###########################################################################
# LAND BOUNDARY CONDITIONS DIRECTORY #
###########################################################################
BCS_PATH : /discover/nobackup/ltakacs/bcs/Icarus-NLv2/Icarus-NLv2_EASE/SMAP_EASEv2_M36/
**** REQUIRED INFO (continued) *****
  2.b) Configure experiment

## Slide 9
###########################################
# Default parameters in GEOSldas_LDAS.rc # ###########################################
#----------------------------------------#
# Rarely changed parameters in GEOSldas #
#----------------------------------------#
# ---- Using offline?
# 1 : yes, offline
#
CATCHMENT_OFFLINE : 1
# ---- No dycore for offline
#
DYCORE : none
# ---- Only one surface level
#
LM : 1
# ---- First ensemble ID
#
FIRST_ENS_ID : 0
# ---- For MAPL_RestartOptional
#
MAPL_ENABLE_BOOTSTRAP : YES
# ---- Vegedyn and catchment default file types
#
VEGDYN_INTERNAL_RESTART_TYPE : binary
CATCH_INTERNAL_RESTART_TYPE : pnc4
CATCH_INTERNAL_CHECKPOINT_TYPE : pnc4
# ---- SURFLAY
#
SURFLAY : 50.0
  2.b) Configure experiment

## Slide 10
  2.b) Configure experiment
#-----------------------------------------------------------#
# Optional parameters. Users can overwrite the defaults #
# through the user-generated exeinp file. #
#-----------------------------------------------------------#
# ---- Metforce time step
# Should be set in the exeinp file where MET_PATH is defined
# 3600 = default
#
FORCE_DTSTEP : 3600
# ---- Choice of Land Surface Model:
# 1 : Catchment Model (Default)
# 2 : CatchmentCN Model
#
LSM_CHOICE : 1
# ---- Time step for carbon/nitrogen routines in CatchmentCN model (default 5400):
# (Time step for water/energy routines is controlled by HEARTBEAT_DT in CAP.rc)
#
# DTCN : 5400

## Slide 11
######################################
# Optional parameters #
######################################
# ---- Domain definition:
# The domain is determined by specifying a lat/lon rectangle in conjunction
# with blacklist and whitelist files. The files contain the IDs of tiles to
# be excluded and included in the domain.
# Included are all tiles within the rectangle or the whitelist but not in the blacklist.
# Default is GLOBAL domain.
#
# Specify extremities of lat/lon rectangle:
# Max lat/lon range: lon=-180:180, lat=-90:90.
# If only whitelist should be used, specify dummy valuessuch that:
# MINLON > MAXLON and MINLAT > MAXLAT.
#
# MINLON : -180.
# MAXLON : 180.
# MINLAT : -90.
# MAXLAT : 90.
#
# Specify path and filenames for blacklist and whitelist files:
# (May leave blank.)
#
# BLACK_FILE : ''
# WHITE_FILE : ''
  2.b) Configure experiment

## Slide 12
######################################
# Optional parameters #
######################################
# ---- Surface layer turbulence scheme:
# 0 : Louis (MERRA, Fortuna-DAS, SMAP NRv4/4.1/5/7.2)
# 1 : Helfand Monin-Obukhov (Fortuna-AR5, Ganymed, Heracles, Icarus-3_2, MERRA-2)
#
CHOOSEMOSFC : 0
# ---- Formulation for turbulent roughness length (Z0):
# 0 : Fortuna, SMAP NRv3
# 1 : Ganymed-4_1, SMAP NRv4/NRv4.1
# 2 : Heracles-4_3, Icarus (AGCM default)
# 3 : SMAP NRv5/NRv7.2
#
Z0_FORMULATION : 3
# ---- ASCAT-derived roughness length:
# 0 : Default - do not use ASCAT information.
# 1 : Replace model roughness length with ASCAT Z0 where climatological NDVI<0.2.
#
USE_ASCATZ0 : 0
  2.b) Configure experiment

## Slide 13
######################################
# Optional parameters #
######################################
# ---- Aerosol deposition on snow (available only with MERRA-2 forcings):
# 0 : DEFAULT, ALL GOCART Aerosol are NOT used
# 1 : use all GOCART aerosol data
# 2 : GOCART DUST is NOT used
# 3 : GOCART Black Carbon is NOT used
# 4 : GOCART Organic Carbon is NOT used
#
AEROSOL_DEPOSITION : 0
# ---- Number of constituents for GOSWIM (the GOddard SnoW Impurity Module)
# 0 : Default, GOSWIM snow albedo scheme is turned OFF for land
# 9 : GOSWIM snow albedo scheme is turned ON for land
#
N_CONST_LAND4SNWALB : 0
  2.b) Configure experiment

## Slide 14
######################################
# Optional parameters #
######################################
# ---- Perturbations (If num_ensemble > 1, PERTURBATIONS will automatically be set to 1):
# 0 : No perturbactions.
# 1 : With perturbations.
#
PERTURBATIONS : 0
# ---- Path to special namelist input files:
# This only applies for ensemble simulations. The variable values in special name list
# overwrite the DEFAULT values . There may be three files:
# LDASsa_SPECIAL_inputs_ensupd.nml,
# LDASsa_SPECIAL_inputs_ensprop.nml, and
# LDASsa_SPECIAL_inputs_catbias.nml
#
# NML_INPUT_PATH : ''
# ---- Write log file (YES/NO)?
#
LDAS_logit : YES
  2.b) Configure experiment

## Slide 15
######################################
# Optional parameters #
######################################
# ---- Job segment length:
# Specify period between output of restart files. (GEOSldas.x shuts down and restarts.)
# Default is the entire simulation period (END_DATE minus BEG_DATE).
# Format: yyyymmdd hhmmss
#
# JOB_SGMT : 00000100 000000
# ---- Number of segments:
# One lenkf.j job simulates NUM_SGMT*JOB_SGMT time, then re-submits itself,
# so (NUM_SGMT*JOB_SGMT) should be done within the 12 hour CPU time limit (at NCCS).
# Low values for NUM_SGMT are recommended for run-time and storage efficiency.
# Default is 1.
#
# NUM_SGMT : 1
  2.b) Configure experiment

## Slide 16
######################################
# Optional parameters #
######################################
# ---- User defined Path and filename of output (HISTORY) specification file:
# If it is empty, ldas_setup will generate default HISTORY.rc.
#
# HISTRC_FILE : ''
# ---- Write monthly output?
# Monthly files can be created from daily files ONLY IF experiment period starts
# and ends at 0z on the first of a month.
# 0 : Output bundled into daily files per HISTORY specifications (default).
# 1 : Monthly files will be created. Daily files will *not* be deleted.
# 2 : Monthly files will be created and daily files will be deleted automatically.
#
# MONTHLY_OUTPUT : 0
# ---- Specify how to interpolate the forcing (Default is 1):
# 1 : bilinear interpolation
# 0 : nearest neighbor
#
MET_HINTERP : 1
  2.b) Configure experiment

## Slide 17
######################################
# Optional parameters #
######################################
# ---- Specify if running model or assimilation:
# NO : model only (DEFAULT; with --runmodel option)
# YES : assimilation (without --runmodel option)
#
LAND_ASSIM : NO
# ---- Choose land model version
# Icarus : Current DEFAULT for the Icarus AGCM (Scientifically close to MERRA-2)
# V24_C05 : DEFAULT for GEOSldas_m4-17_0
# NRv7.2 : Current DEFAULT beginning with GEOSldas_m4-17_6
#
LAND_PARAMS : NRv7.2
# ---- File name for mwRTM parameter file (nc4 format) used in assimilation runs.
# This file can be converted from binary with the program mwrtm_bin2nc4.x.
# If empty or commented out, GEOSldas will search the restart directory.
#
# MWRTM_FILE : ''
  2.b) Configure experiment
NOTE:
Beginning with GEOSldas_m4-17_7, LAND_PARAMS replaces the LAND_UPD compiler flag of earlier tags.

## Slide 18
  Edit the sample input file YOUR_batinp.txt created by the following command:
  ./ldas_setup sample –-batinp > YOUR_batinp.txt)
# REQUIRED inputs
#
# NOTE:
# (1) rm_name (resource manager name) is SLURM (PBS is no longer used)
# (2) walltime is in the format hh:mm:ss
#
rm_name :
account :
walltime :
ntasks :
#
# OPTIONAL inputs
#
# NOTE:
# (1) Default job_name is "exp_id"
# (2) Default constraint is "hasw"
# (3) Do not specify qos (quality-of-service) by default. Specify "debug" for faster but limited service.
#
#job_name :
#constraint :
#qos :
  2.c) Configure computing

## Slide 19
go to $ESMADIR/src/Applications/LDAS_App/ or $ESMADIR/Linux/bin, soure g5_modules if it is a new terminal window:
./ldas_setup setup [--runmodel] YOUR_EXPDIR YOUR_exeinp.txt YOUR_batinp.txt
YOUR_EXPDIR, YOUR_exeinp.txt, and YOUR_batinp.txt must be ordered as above (positional arguments).
Use option --runmodel for model-only runs (no assimilation).
Running ldas_setup creates the folder YOUR_EXPDIR/EXP_ID/ and its sub-structures. Configuration input files, such as cap_restart, CAP.rc, HISTORY.rc, and LDAS.rc are created in the ./run subdirectory.
All Fortran binary output created by GEOSldas is in the operating system’s native endian format (little endian at NCCS).
  2.d.1) Run ldas_setup to create a model run

## Slide 20
Before running ldas_setup, the file mwrtm_param.nc4 must be created in netcdf format, unless the file is already in the restart directory or the assimilation configuration does not require it (e.g., if retrievals instead of brightness temperatures are assimilated).
Use the program $ESMADIR/Linux/bin/mwrtm_bin2nc4.x to convert a binary mwRTM file into nc4.
Go to $ESMADIR/src/Applications/LDAS_App/ or $ESMADIR/Linux/bin
./ldas_setup setup YOUR_EXPDIR YOUR_exeinp.txt YOUR_batinp.txt
The input parameter LAND_ASSIM must be YES.
If L-band brightness temperatures are assimilated, the input parameter MWRTM_FILE must point to an mwRTM parameter file in nc4 format unless an mwRTM file is already included in the restart directory.
There may be up to three nml configuration files in NML_INPUT_PATH:
LDASsa_SPECIAL_inputs_ensupd.nml
LDASsa_SPECIAL_inputs_ensprop.nml
LDASsa_SPECIAL_inputs_catbias.nml
  2.d.2) Run ldas_setup to create an assimilation run

## Slide 21
BEG_DATE: 20120101 000000
END_DATE: 20160101 000000
JOB_SGMT: 00000100 000000
NUM_SGMT: 6
HEARTBEAT_DT: 450
YYYYMMDD HHMMSS:
Restart file frequency.
The BEG_DATE in CAP.rc will be ignored. GEOSldas reads BEG_DATE from cap_restart.
JOB_SGMT is the time period between output of check-point files, which can be used as restart files.
The wall time needed for running a simulation period of NUM_SGMT*JOB_SGMT must not exceed the wall time limit (12 hours at NCCS).
Seconds (SS) in *_DATE and JOB_SGMT should be set to 00 because GEOSldas restart file names do not contain seconds.
CAP.rc
  2.e) Resource files generated by ldas_setup

## Slide 22
  2.e) Resource files generated by ldas_setup
HISTORY.rc HEADER
EXPID: m36_SMAP
EXPDSC: GEOSldas_output
EXPSRC: GEOSldas_m4-17_0
COLLECTIONS:
'tavg1_1D_lnd_Nt'
'tavg1_1D_lfs_Nt‘
'tavg1_2D_lnd_Nx'
'tavg1_2D_lfs_Nx'
::
Sample ‘lnd’ tile-spaced collection header:
tavg1_1D_lnd_Nt.descr: 'Land diagnostics' ,
tavg1_1D_lnd_Nt.template: '%y4%m2%d2_%h2%n2z.bin' ,
tavg1_1D_lnd_Nt.mode: 'time-averaged' ,
tavg1_1D_lnd_Nt.frequency: 240000 ,
tavg1_1D_lnd_Nt.ref_time: 000000,
tavg1_1D_lnd_Nt.fields: 'WET3' ,'CATCH' ,'GWETPROF' ,
::
Sample ‘lnd’ 2D collection header:
tavg1_2D_lnd_Nx.descr: '2D-space,Land Diagnostics' ,
tavg1_2D_lnd_Nx.template: '%y4%m2%d2_%h2%n2z.nc4' ,
tavg1_2D_lnd_Nx.mode: 'time-averaged' ,
tavg1_2D_lnd_Nx.frequency: 240000 ,
tavg1_2D_lnd_Nx.ref_time: 000000,
tavg1_2D_lnd_Nx.format: 'CFIO',
tavg1_2D_lnd_Nx.regrid_exch:'../input/tile.data'
tavg1_2D_lnd_Nx.regrid_name: 'GRIDNAME'
tavg1_2D_lnd_Nx.resolution: 720 361,
tavg1_2D_lnd_Nx.deflate: 2,
tavg1_2D_lnd_Nx.fields: 'WET3‘ , 'CATCH' ,
::
  HISTORY.rc (output file format is always nc4)
Output at sub-daily frequency will be bundled into daily output files.
Monthly output will be created from daily files if requested(see MONTHLY_OUTPUT option).

## Slide 23
  More on HISTORY.rc output options:
  ldas_setup produced CAP.rc and HISTORY.rc, which can be modified before starting a simulation. There are two lists of pre-defined output collections in HISTORY.rc: (i) lnd (matching lnd in MERRA-2 and GEOS FP and LDASsa out_collection_id =5 in LDASsa) and (ii) lfs (land forcings and states), each defined separately for 2D or tile-space (vector) outputs.
  1) The following Collections provide 1-hourly average, gridded output at the native resolution (Nx). 2D does NOT work for EASE grids.
  COLLECTIONS:
  'tavg1_2D_lnd_Nx'
  'tavg1_2D_lfs_Nx'
  ::
  2) The following Collections provide 1-hourly average, tile-space output in native tile space (Nt). Use, e.g., for EASE grids.
  COLLECTIONS:
  'tavg1_1D_lnd_Nt'
  'tavg1_1D_lfs_Nt'
  ::
  3) Gridded and tile-space output can be requested together, e.g.:
  COLLECTIONS:
  'tavg1_1D_lnd_Nt’
  'tavg1_2D_lnd_Nx’
  ::
  2.e) Resource files generated by ldas_setup

## Slide 24
  More on HISTORY.rc output options (continued):
  4) If you don't want any output, use ’#’ to comment out the header (or just delete those lines):
  COLLECTIONS:
  # 'tavg1_1D_lnd_Nt'
  # 'tavg1_1D_lfs_Nt'
  # 'tavg1_2D_lnd_Nx'
  # 'tavg1_2D_lfs_Nx'
  ::
  5) If you want ’lnd’ output but not ‘lfs’, comment out ‘lfs’ (or just delete the line):
  COLLECTIONS:
  'tavg1_1D_lnd_Nt'
  # 'tavg1_1D_lfs_Nt'
  ::
  2.e) Resource files generated by ldas_setup

## Slide 25
  More on HISTORY.rc output options (continued):
  6) If you just want to write out a few variables, simply comment out what you do not want in the output. Note that the double colon sign (::) separates lists and should not be touched. E.g., the list below only writes out only Tair and RainfSnowf in the tile-space ‘lfs’ Collection:
  tavg1_1D_lfs_Nt.template: '%y4%m2%d2_%h2%n2z.bin',
  tavg1_1D_lfs_Nt.archive: '%c/Y%y4',
  tavg1_1D_lfs_Nt.mode: 'time-averaged',
  tavg1_1D_lfs_Nt.frequency: 240000,
  tavg1_1D_lfs_Nt.ref_time: 000000,
  tavg1_1D_lfs_Nt.fields: 'Tair’ , 'DATAATM' ,
  # 'Qair' , 'DATAATM' ,
  # 'LWdown' , 'DATAATM' ,
  # 'SWdown' , 'DATAATM' ,
  # 'Wind' , 'DATAATM' ,
  # 'Psurf' , 'DATAATM' ,
  # 'Rainf_C' , 'DATAATM' ,
  # 'Rainf' , 'DATAATM' ,
  # 'Snowf' , 'DATAATM' ,
  'RainfSnowf' , 'DATAATM' ,
  # 'SWnet' , 'DATAATM' ,
  # 'RefH' , 'DATAATM' ,
  # 'CATDEF' , 'CATCH’ ,
  # 'RZEXC' , 'CATCH’ ,
  # 'SRFEXC' , 'CATCH’ ,
  # 'WESNN1' , 'CATCH’ ,
  # 'WESNN2' , 'CATCH’ ,
  # 'WESNN3' , 'CATCH’ ,
  # 'HLWUP' , 'CATCH’ ,
  ::
  2.e) Resource files generated by ldas_setup

## Slide 26
  More on HISTORY.rc output options (continued):
  7) Mode can be ‘time-averaged’ or 'instantaneous’ (snapshot).
  8) You can choose the reference time.
  9) For ‘2D’ Collections, you can change the resolution (e.g., 720x361, 360x181, 576x361, …). (Note that 2D does not work for EASE grids.)
  10) Do NOT change the file name extension. It should always be 'bin' for tile-space and 'nc4' for 2D output.
  2.e) Resource files generated by ldas_setup

## Slide 27
Note:
1) This file combines the default values and values specified in YOUR_exeinp.txt.
2) Users are discouraged from editing LDAS.rc. However, it is safe to just change the met_tag and met_path. The met_path is a link. So users need to change the link in the directory ../input/met_forcing too.
3) For explanation of the parameters, use the ldas_setup command under Linux/bin or Application/LDAS_App.
./ldas_setup sample –-exeinp
LDAS.rc (incomplete)
CATCHMENT_OFFLINE: 1
DYCORE: none
LM: 1
FIRST_ENS_ID: 0
Z0_FORMULATION: 3
CHOOSEMOSFC: 0
PERTURBATIONS: 0
LDAS_logit: YES
MAPL_ENABLE_BOOTSTRAP: YES
AEROSOL_DEPOSITION: 0
LAND_ASSIM: NO
SURFLAY: 50.0
MET_HINTERP: 1
LAND_PARAMS: NRv7.2
MET_TAG: M2COR_cross
MET_PATH: ../input/met_forcing/MERRA2_land_forcing
FORCE_DTSTEP: 3600
GRIDNAME: SMAP-EASEv2-M36
RESOLUTION: SMAP_EASEv2_M36
LSM_CHOICE: 1
NX: 28
NY: 1
IMS_FILE: IMS.rc
CATCH_INTERNAL_RESTART_FILE: ../input/restart/catch_internal_rst
CATCH_INTERNAL_RESTART_TYPE: pnc4
VEGDYN_INTERNAL_RESTART_FILE: ../input/restart/vegdyn_internal_rst
VEGDYN_INTERNAL_RESTART_TYPE: binary
CATCH_INTERNAL_CHECKPOINT_FILE: catch_internal_checkpoint
CATCH_INTERNAL_CHECKPOINT_TYPE: pnc4
  2.e) Resource files generated by ldas_setup

## Slide 28
How does lenkf.j work?
TSTEPS_PER_SGMT = JOB_SGMT (in seconds) / HEARTBEAT_DT
The begin date is in cap_restart.
JOB_SGMT is the time period to output checkpoints or restart files.
(NUM_SGMT*JOB_SGTMT) is the simulation time period for which execution fits within the wall time limit (12 hours at NCCS).
For each JOB_SGTMT time, GEOSldas advances cap_restart, re-links the restart file and post-processes the outputs, i.e., transforms binary to nc4, concatenates into daily files, etc.
After (NUM_SGMT*JOB_SGTMT), lenkf.j re-submits itself and repeats from step 1 until the END_DATE.
Execute the following command: YOUR_EXPDIR/EXP_ID/run/sbatch lenkf.j
Note that lenkf.j itself is executable. Users can launch it directly using the command ./lenkf.j in interactive mode (see debugger instructions below on how to get compute nodes using xalloc).
Q & A :
What if an NCCS downtime or some other reason kills my job before the simulation is complete?
Go to YOUR_EXPDIR/EXP_ID/run/ and verify that cap_restart matches the time stamp in the link ../input/restart/catch_internal_rst, then run “sbatch lenkf.j”
What if I decide to extend the simulation beyond the initially set END_DATE?
Go to YOUR_EXPDIR/EXP_ID/run, change END_DATE in CAP.rc and run “sbatch lenkf.j”
Can I change the ntasks after ldas_setup?
Yes. Change the following line in lenkf.j
#SBATCH --ntasks=xxx
  2.f) Run GEOSldas

## Slide 29
EXP ID | JOB_SGMT | NUM_SGMT | Wall time | Description
Exp_A | 00000100 000000 (monthly restarts) | 1 | 7m 25s | The longer JOB_SGMT is more efficient. But the job will have to restart from the beginning of the month if it is interrupted for any reason.
Exp_B | 00000001 000000 (daily restarts) | 31 | 15m 17s | Small values for JOB_SGMT are inefficient because of the overhead needed to frequently restart the GEOSldas executable. Storage may also be an issue if many restarts are written.
How are JOB_SGMT and NUM_SGMT set to make the run efficient?
The table below lists an example for a Catchment simulation on the M36 global domain with two default HISTORY collections of daily output using 56 processors.
The two experiments are identical except that Exp_A writes monthly restarts, and Exp_B writes daily restarts.
The results illustrate that it is not efficient to write many restarts within a single 12-hour NCCS job window. The job runs most efficiently when NUM_SGMT=1 and JOB_SGMT is such that one GEOSldas.x job (for the period NUM_SGMT*JOB_SGMT) finishes within 12 hours of wall time.
Note that restarts (especially the carbon restarts needed for CatchmentCN) are large files.
If only some restart variables are needed for later analysis, users should create a custom file collection using the HISTORY.rc functionality.
  2.f) Run GEOSldas
Notes: 12m56.650s for two days , i.e.
00000000 010000
NUM_SGMT:48

## Slide 30
  2.g) Use graphic debugger tools
To use debugging applications (e.g., Totalview and DDT), GEOSldas should be compiled with the BOPT=g option, i.e.,
  make install BOPT=g
  Don’t forget to make clean first.
  Parallel_build can also build with bdubbign flags, build in build-Debug/ and install into install-Debug/:
  parallel_build.csh -debug
Get an interactive job using the following command:
  xalloc --ntasks=56 --time=01:00:00 --account=g0610 –-constraint=hasw
  Users should use their own account and choose ntasks and time.
Users can launch “lenkf.j 1” for Totalview or “lenkf.j 2” for DDT to debug the program interactively.
Once launched, configure the run (GEOSldas uses OpenMPI implementation), set breakpoints and start debugging.
Note: Debuggers may run out of licenses if too many processors are used ( 28 processors are recommended).

## Slide 31
  2.h) Documentation and utilities for post-processing
Documentation is in:
./src/Applications/LDAS_App/doc
Documentation includes this tutorial and README files.
Utilities for post-processing are in:
./src/Applications/LDAS_App/util
For now, this directory includes select matlab scripts that were inherited from LDASsa. Users are encouraged to submit useful scripts to be added into this directory.

## Slide 32
3. Land Model Versions
Catchment model version:
Beginning with GEOSldas_m4-17_7, the Catchment model version can be selected through the LAND_PARAMS input parameter. Current options are:
  Icarus : Current DEFAULT for the Icarus AGCM (Scientifically close to MERRA-2)
  V24_C05 : DEFAULT for GEOSldas_m4-17_0
  NRv7.2 : Current DEFAULT since GEOSldas_m4-17_6
The “SMAP NRv7.2” version of the Catchment model is the current default. The “Icarus” option is similar but not identical to the MERRA-2 version of the Catchment model.

## Slide 33
Boundary conditions (bcs):
There are new bcs to go with the “NRv7.2” version of the Catchment model (see subsequent slides).
/discover/nobackup/ltakacs/bcs/Icarus-NLv2/
/discover/nobackup/ltakacs/bcs/Icarus-NL/
The “NL” bcs were used for generating NRv7.2 output and are used in the Version 4 SMAP L4_SM system. The “NLv2” bcs are used by default in GEOSldas_m4-17_7 and include a minor patch that addresses the spatial inter- and extrapolation of the vegetation greenness fraction and the vis/nir diffuse albedo parameters. Specifically, in the “NL” version these parameters were poorly defined for tiles that are land in Globcover2009 but not land according to GLCCv2.0, for which the greenness and vis/nir diffuse parameters were available.
GEOSldas can also be run with older versions of the bcs. Note, however, that GEOSldas requires some bcs files (NDVI and vegdyn) that did not exist in earlier bcs versions. The following bcs:
/discover/nobackup/ltakacs/bcs/Ganymed-4_0/Ganymed-4_0_MERRA-2/
/discover/nobackup/projects/gmao/ssd/land/l_data/geos5/bcs/CLSM_params/mkCatchParam_SMAP_L4SM_v001
/discover/nobackup/projects/gmao/ssd/land/l_data/geos5/bcs/CLSM_params/mkCatchParam_SMAP_L4SM_v002
were patched to work with GEOSldas (and still work with LDASsa). Upon request, Sarith can patch old bcs directories.
3. Land Model Versions

## Slide 34
 | LDASsa | GEOSldas
Catchment | X | X
CatchmentCN (incl. carbon/nitrogen processes) |  | X
River routing |  | 
Snow impurity module (GOSWIM) |  | X
Data assimilation | Catchment | Catchment
3. Land Model Versions
Availability of model and assimilation components in GEOSldas_m4-17_7:

## Slide 35
Parameter | Icarus-2_0_p1 (and MERRA-2*) | Icarus-NLv2 (“New Land”)
Soil | NGDC (5-arcmin texture with 12 soil types) | HWSD (30-arcmin texture with 253 soil types)
Topography | HYDRO1k | Hybrid of SRTM and other (where SRTM is not available)
LAI | GSWP2 (AVHRR NDVI based 1-degree, monthly climatology from 1982-1998) | Merged MODIS v005(MCD43GF) and GEOLAND2 (30-arcsec, 8-day climatology from 2000-2014)
Greenness | AVHRR | AVHRR (see earlier slide for diff between “NL” and “NLv2” bcs)
Albedo | MODIS | MODIS (see earlier slide for diff between “NL” and “NLv2” bcs)
Landcover | GLCCv2 (aggregated from 30-arcsec to 2.5min) (mosaic only) | GLOBCOVER 2009 (10-arcsec) (mosaic, CLM4, CLM4.5)
Watersheds | HYDRO1k based 36,716 Level-6 Pfafstetter catchments on a 2.5-arcmin land-ice-lake-ocean mask | SRTM based 291,284 Level-12 Pfafstetter catchments (resulting in finer resolution tiles) on a 10-arcsec land-ice-lake-ocean mask
Canopy Height | Look-up table [= f(veg type)] | JPL (30-arcsec)
Roughness (Z0) | Function of effective canopy height | ASCAT Z0 (0.1ox0.1o) (by DEFAULT not used in GEOSldas_m4-17_7)
NDVI | Not used | NDVI3g (5-arcmin, 15-day climatology from 1981-2015) (by DEFAULT not used in GEOSldas_m4-17_7)
Location on Discover | /discover/nobackup/ltakacs/bcs/Ganymed-4_0/Ganymed-4_0_MERRA-2/ | 
 |  | /discover/nobackup/ltakacs/bcs/Icarus-NLv2/
*See also Table 2 of Reichle et al. 2017, Assessment of MERRA-2 Land Surface Hydrology Estimates, J Climate (doi:10.1175/JCLI-D-16-0720.1) |  | 
3. Land Model Versions

## Slide 36
Parameter | Icarus-2_0_p1 (*MERRA-2) | GEOSldas_m4-17_0 (Sarith’s v24_C05_GOSWIMplus) | GEOSldas_m4-17_7 (and *17_6) (NRv7.2)
WEMIN | 26 | 13 | 13
AICEV (relevant to snow cover fraction mapping) | 0.149 | 0.107 | 0.107
AICEN (relevant to snow cover fraction mapping) | 19.851 | 19.893 | 19.893
CSOIL_2 (heat capacity of surface ground layer) | 200 | 70,000 (re-introduces pre-MERRA value; implies DZ_TSURF=0.05m) | 70,000
RSSWILT IN SUBROUTINE RSURFP2 | 500 | 2,000 | 500
ASTRFR IN SUBROUTINE ENERGY2 | 0.333 | 1. | 0.333
STEXP IN SUBROUTINE ENERGY2 | 1. | 2. | 1
IN SUBROUTINE RZDRAIN | n/a | IF(SRFLW < 0.) SRFLW = 0.01*SRFLW | IF(SRFLW < 0.) SRFLW = 0.04*SRFLW
IN SUBROUTINE RZDRAIN | RZAVE <= 0. | RZAVE <= 1.e-4 | RZAVE <= 1.e-4
SUBROUTINE BASE | AMIN1(cond) | Unit correction no effect AMIN1(1000.*cond) | Unit correction no effect AMIN1(1000.*cond)
catchment.F90 | Dampen oscillations (except ITYP=1) | Dampen oscillations for all types | Dampen oscillations for all types
*See also Table 2 of Reichle et al. 2017, Assessment of MERRA-2 Land Surface Hydrology Estimates, J Climate (doi:10.1175/JCLI-D-16-0720.1) |  |  | 
3. Land Model Versions

## Slide 37
Parameter | Icarus-2_0_p1 (*MERRA-2) | GEOSldas_m4-17_7 (and *17_6 and *17_0) (NRv7.2 and Sarith’s v24_C05_GOSWIMplus)
Thermal conductivity bug fix | Bug | Fixed
Calculation of effective vegetation height for use in roughness height and displacement height estimates | ZVG = {Z2 – (Z2 – MIN_VEG_HEIGHT)} * exp (-LAI) where Z2 is canopy height & MIN_VEG_HEIGHT=0.01 ZOT = 0.13 * ZVG * s (Icarus: s=2; MERRA-2: s=1) DOT = 0.66 *ZVG Icarus (up to and including Icarus-3_2) has effectively Z0_FORMULATION=2, with Z2 from look-up table. MERRA-2 has effectively Z0_FORMULATION=0. | ZVG = {Z2 – 0.5 * (Z2 – MIN_VEG_HEIGHT)} * exp (-LAI) where Z2 is canopy height & MIN_VEG_HEIGHT=0.01 ZOT = 0.13 * ZVG DOT = 0.66 *ZVG Z0_FORMULATION=3, with Z2 meant to be from JPL Lidar canopy height dataset. Unintentionally, the default in GEOSldas_m4-17_6 and *17_0 was Z0_FORMULATION=2.
Surface roughness length | Above ZOT. | Above ZOT. (Optionally can use ASCAT Z0 wherever climatological NDVI is less than 0.2.)
GOSWIM (GOddard SnoW Impurity Module) | Not available | Available
Surface specific humidity limits in catchment.F90 and GEOS_CatchGridComp.F90 (Andrea Molod) | Not applied | Applied
*See also Table 2 of Reichle et al. 2017, Assessment of MERRA-2 Land Surface Hydrology Estimates J Climate (doi:10.1175/JCLI-D-16-0720.1) |  | 
3. Land Model Versions

## Slide 38
  4. Additional Parameters for the AGCM
LIST OF SURFACE PARAMETERS
###########################################################################
# #
###########################################################################
# ----------------
# CO2 coupling
# ----------------
# USE_CNNEE: 0 # options : 0 (default); 1 (Chem uses NEE from CatchmentCN, # NOTE you must add USE_CNNEE: 1 to CO2_GridComp.rc, CMIP/CO2_GridComp.rc,
# MERRA2/CO2_GridComp.rc, MERRA2/19600101-20000331/CO2_GridComp.rc, MERRA2/20000401- # present/CO2_GridComp.rc, and PIESA/CO2_GridComp.rc in # /GEOSchem_GridComp/GOCART_GridComp/CO2_GridComp/ before you build the model.)
# USE_CO2SC: 0 # options : 0 (default); 1 (CatchmentCN uses CO2SC from Chem, # NOTE you must set doing_CO2: yes in $EXPDIR/RC/Chem_Registry.rc )